## Slide 1: W3C Web of Things Thing Description for API Description of IoT Devices
Ege Korkan - TU Munich | W3C WoT Working Group
API Specifications Conference 2020 - 09.09.2020

## Slide 2: What is IoT, in this talk?
IP based
IP based
Local Network
Zigbee,
Bluetooth ...
IP Router
Gateway

## Slide 3: What is IoT, in this talk? An example
ZigBee
REST Client
https://www.gravis.de/out/pictures/z1/philips-hue-white-26amp-color-ambiance-starter-kit-3x-gu10-bridge-bluetooth_z1.jpg
HTTP
IP Router

## Slide 4: What is IoT, in this talk?
IP based
Local Network
IP based
Examples from:
Oracle
Microsoft Azure
Amazon AWS
IP Router

## Slide 5: What is IoT, in this talk?
IP based
IP based
Local Network
My Gateway
Examples from:
Mozilla WebThing
SmartThings
OpenHAB
HomeAssistant
Thingworx
IP Router

## Slide 6: To summarize
The communication to the public Internet happens always via IP level protocols such as:
  HTTP
  MQTT
  WebSockets, etc.
The communication in the local network happens via many different non-IP and IP level protocols such as:
  HTTP, MQTT, CoAP, WebSockets
  Industrial protocols: OPC-UA, Modbus TCP, BacNet
  Non-IP protocols: Bluetooth, Zigbee, LoRaWAN
Additional silos due to different verticals also exist
Notes: say that local networks also have discovery

## Slide 7: Our Goal: Support Mashups
but in the IoT!
Notes: give examples of IoT mashups. Maybe figures?

## Slide 8: Web of Things to help! - Initial Ideas
Was a proposal on how to build REST APIs for IoT devices
Is about describing any kind of API for IoT devices

## Slide 9: Standardization via Thing Descriptions!
Abstract description of network APIs of IoT devices
  Property
  Action
  Event
Semantic annotation of capabilities by other vocabularies over the Web: schema.org, SSN, ...
Concrete protocol description of individual devices

## Slide 10: Example TD: Thing Level
{
"@context": [
"https://www.w3.org/2019/wot/td/v1",
{"iot":"http://iotschema.org"}
],
"@type":"SprinklerStation",
"id": "urn:dev:ops:Agriculture-7331",
"title": "SoilStation",
"description": "A soil management station for use in agriculture",
"securityDefinitions": { "basic_sc": {"scheme": "basic"} },
"security": "basic_sc",
"properties": {
"temperature": {...}
},
"actions": {
"startSprinkler": {...}
},
"events": {
"tooDry": {...}
},
"links":["href":"docs", "rel":"about", "type":"text/html"]
}
Thing
Metadata
Definitions of
Interaction Affordances
Semantic Annotations
Security
Metadata
Links to other
Documents

## Slide 11: Example TD: Interaction Level
"properties": {
"temperature": {
"title": "Temperature",
"type": "number",
"unit": "Celsius",
"forms": [...]
}
},
"actions": {
"startSprinkler":{
"description": "Run sprinkler for a set time",
"input": {
"type": "object",
"properties": {"timeout": {...}},
},
"forms": [...]
},
"events": {
"tooDry": {
"data": {"type": "string"},
"forms": [...]
}
}
Interaction
Metadata
JSON Schema
Concrete
Protocol Information

## Slide 12: Example TD: Protocol Bindings
{
"forms": [
{
"href": "http://example/light/currentdimmer",
"contentType": "application/json",
"op": "readproperty",
"htv:methodName": "GET"
},
{
"href": "mqtt://example.com/example/light/currentdimmer",
"op": "observeproperty",
"mqv:controlPacketValue": "SUBSCRIBE"
}
]
}
Protocol and URI
of the Resource
Intended WoT
Operation
Protocol Specific Vocabulary

## Slide 13: Specification

## Slide 14: TD Playground
http://plugfest.thingweb.io/playground/

## Slide 15: Related to

## Slide 16: What can you do with TDs: Scripting
Interact with Things without thinking about the protocol !
Possible via WoT Scripting API and its implementation node-wot
https://github.com/eclipse/thingweb.node-wot
A tutorial: https://www.youtube.com/watch?v=wDX45dsD4GM

## Slide 17: What can you do with TDs: UI Generation
Simple demo hosted at http://plugfest.thingweb.io/webui/
Notes: Browser based

## Slide 18: What can you do with TDs: UI Generation
Available at https://github.com/tum-esi/wade
Notes: electron + Vue application, extensible

## Slide 19: What can you do with TDs: Orchestration
Full video at: https://w3c.github.io/wot-marketing/developers/wot_nodegen.mp4
Node-RED Node generator:
- Flow based programming and orchestration tool
- Generate nodes from OpenAPI or TD documents
- Officially supported by OpenJS Foundation

## Slide 20: What can you do with TDs
MASHUPS!

## Slide 21: Mashups in WoT
Bringing devices together (from different manufacturers) to perform bigger tasks

## Slide 22: Mashups in WoT

## Slide 24: More for WoT Developers!
WoTify: a collection of open-source devices that have been WoT-enabled, at wotify.org
WoT Application Manager (WAM): Jumpstart your WoT applications, similar to Vue CLI and similar ones
td-code: VS Code extension that allows TD validation, completion
WoT-Testbench: Automatic Thing black-box testing from its TD
Shadow Thing: No-code Thing simulation and proxying

## Slide 25: Going further with the WoT Standardization
Discovery
  Registration, Management, Notification and Search API for TD databases
  Network level service discovery
TD new features
  Templating mechanisms
  Better OAuth2 support
  Support more complex eventing mechanisms
Scripting API
  Stable core API
  Work on higher level APIs

## Slide 26: How to join
Weekly calls on Wednesdays for the entire Working Group and guests
Each Task Force has their own calls, weekly or bi-weekly
W3C TPAC 2020 is on October! https://www.w3.org/2020/10/TPAC/

## Slide 27: Summary
Goal: Overcome domain silos, increase interoperability between IoT stakeholders, and enable cross domain IoT applications
  Similar to what the Web is for the Internet!
About 200 members
Normative work on technology building blocks (Thing Description, Architecture, Binding Templates, Scripting API, Security, Discovery)
PlugFests/ Hackathons every 3-4 months
New charter has just started, come join us!

## Slide 28: Contact
W3C Web of Things Working Group:
Main Page: https://www.w3.org/WoT/
W3C Contact:
  Kaz Ashimura (ashimura@w3.org)
Co-Chairs:
  Michael McCool (michael.mccool@intel.com)
  Sebastian Käbisch (sebastian.kaebisch@siemens.com)
Me:
GitHub and Twitter: @egekorkan
Email: egekorkan@gmail.com
Personal Website: egekorkan.com