## Slide 1: Web of Things in the Smart City
Michael McCool
June 2021

## Slide 2: W3C Web of Things (WoT)
W3C WoT Working Group goal: Adapting web technologies to IoT
Published: Thing Description (TD) metadata format
  TD describes the available interactions (network API) of a Thing
In Progress: TD 1.1 Update, Thing Models, Discovery, Profiles
  How to obtain TDs? How to ensure interoperability?
App
App
App
HTTP
MQTT
Modbus
WS
AMQP
OPC-UA
KNX
BACnet
ECHONET
JSON
XML
EXI
CBOR
OAUTH2
API Key
Bearer
TLV
App
App
App
{ properties, actions, events }
WoT API
WoT API
WoT API
HTTP
MQTT
Modbus
WS
AMQP
OPC-UA
KNX
BACnet
ECHONET
JSON
XML
EXI
CBOR
OAUTH2
API Key
Bearer
TLV

## Slide 3: WoT Thing Descriptions
{
"@context": [
"https://www.w3.org/ns/td",
{ "iot": "http://iotschema.org/" }
],
"id": "urn:dev:ops:32473-WoTLamp-1234",
"title": "MyLEDThing",
"description": "RGB LED torchiere",
"@type": ["Thing", "iot:Light"],
"securityDefinitions": ["default": {
"scheme": "bearer"
}],
"security": ["default"],
"properties": {
"brightness": {
"@type": ["iot:Brightness"],
"type": "integer",
"minimum": 0,
"maximum": 100,
"forms": [ ... ]
}
},
"actions": {
"fadeIn": {
...
Door = Thing
Handle = Affordance
What?
How?
Open
Pull
Turn
  WHAT the possible choices are
    Properties
    Events
    Actions
  HOW to interact with the Thing
    Protocol operations and options
    Data schemas and content types
    Security requirements

## Slide 4: Usage Patterns

## Slide 5: Smart City Use Cases
Visitor Guidance
Energy Management
Retail Services
Health
Others
  Law Enforcement
  Parking
  Accessibility
  Traffic and Logistics
  Public Transportation
  Air Quality and Weather
  Cultural Space Mgmt
  Construction Services
  Land Management
  Emergency Services
  Water Management
  Hybrid Ruralization

## Slide 6: Contacts
Dr. Michael McCool
Principal Engineer
Intel
Technology Pathfinding
michael.mccool@intel.com
Dr. Sebastian Kaebisch
Senior Key Expert
Siemens
Technology
sebastian.kaebisch@siemens.com
https://www.w3.org/WoT

## Slide 7: Backup

## Slide 8: Image Credits
Solar Installation Vietnam: By Intel Free Press - https://www.flickr.com/photos/intelfreepress/7169063498/sizes/o/in/photostream/, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=28011974
Telemedicine Consult: By Intel Free Press - https://www.flickr.com/photos/intelfreepress/6948764580/sizes/o/in/photostream/, CC BY 2.0, https://commons.wikimedia.org/wiki/File:Telemedicine_Consult.jpg

## Slide 9: Documents and Resources
New/Updated Normative Documents in Draft Status:
Architecture 1.1: https://github.com/w3c/wot-architecture
Thing Description 1.1: https://github.com/w3c/wot-thing-description
Discovery: https://github.com/w3c/wot-discovery
Profiles: https://github.com/w3c/wot-profile
New/Updated Informative Documents in Draft Status:
Binding Templates: https://github.com/w3c/wot-binding-templates
Scripting API: https://github.com/w3c/wot-scripting-api
Use Cases and Requirements: https://github.com/w3c/wot-usecases
Other Resources:
Web Site: https://www.w3.org/WoT/

## Slide 10: WoT Orchestration
Node-RED/node-gen
node-wot/Scripting API
WoTHelpers.fetch( "coap://localhost:5683/counter" ).then( async (td) => {
// using await for serial execution (note 'async' in then() of fetch())
try {
let thing = await WoT.consume(td);
console.info( "=== TD ===" );
console.info(td);
console.info( "==========" );
// read property #1
let read1 = await thing.readProperty( "count" );
console.info( "count value is" , read1);
// increment property #1 (without step)
await thing.invokeAction( "increment" );
let inc1 = await thing.readProperty( "count" );
console.info( "count value after increment #1 is" , inc1);
// increment property #2 (with step)
await thing.invokeAction( "increment" , {'step' : 3});
let inc2 = await thing.readProperty( "count" );
console.info( "count value after increment #2 (with step 3) is" , inc2);
// decrement property
await thing.invokeAction( "decrement" );
let dec1 = await thing.readProperty( "count" );
console.info( "count value after decrement is" , dec1);
} catch(err) {
console.error( "Script error:" , err);
}
}).catch( (err) => { console.error( "Fetch error:" , err); });

## Slide 11: Current WoT WG Charter Work Items
Architectural Requirements, Use Cases, and Vocabulary
  Understand and state requirements for new use cases, architectural patterns, and concepts.
Link Relation Types:
  Definition of specific link relation types for specific relationships.
Observe Defaults:
  For protocols such as HTTP where multiple ways to implement "observe" is possible, define a default.
Implementation View Spec:
  More fully define details of implementations.
Interoperability Profiles:
  Support plug-and-play interoperabilty via a profile mechanism
  Define profiles that allow for finite implementability
Thing Models:
  Define how Thing Descriptions can defined in a modular way.
Complex Interactions:
  Document how complex interactions can be supported via hypermedia controls.
Discovery:
  Define how Things are discovered in both local and global contexts and Thing Descriptions are distributed.
Identifier Management:
  Mitigate privacy risks by defining how identifiers are managed and updated.
Security Schemes:
  Vocabulary for new security schemes supporting targeted protocols and use cases.
Thing Description Vocabulary:
  Extensions to Thing Description vocabulary definitions.
Protocol Vocabulary and Bindings:
  Extensions to protocol vocabulary definitions and protocol bindings.